## Slide 1: GIS Lesson 11
Spatial Analysis (3) – Service Area Analysis
空間分析 (3) – 服務區分析
2020/7/29

## Slide 2: Agenda
1. Today’s Class 今日課堂
2. Tutorial 個別指導
Service Area Analysis – 服務區分析
Follow tutorial here: https://www.qgistutorials.com/en/docs/3/service_area_analysis.html
Example coursework
Demonstration in QGIS
What is Service Area Analysis?
How is service area analysis used in real life?

## Slide 3: Video – Service Area Time Lapse (15 min travel time by walking from downtown Cincinaati)(0:07)
Notes: Available buses changes throughout the day
The area reachable changes significantly

## Slide 4: What is Service Area Analysis (SAA)?
Service Area: a region that covers all streets accessible by certain travel mode(s), such as walking, cycling and driving.
  For example, a 10-minute service area for a point on a network contains all the streets that can be reached within 10 minutes from that point.
Service Area Analysis:
  Is a type of network analysis that determines all accessible streets within a time interval
  Can assess the travel time from selected points in a network
  Mainly uses the travel speed data available in datasets for computation
  Can be done in both ArcGIS and QGIS
Source: https://desktop.arcgis.com/en/arcmap/latest/extensions/network-analyst/service-area.htm#ESRI_SECTION1_DEC185407C154056B6B17077F9BAD8F2

## Slide 5: How is Service Area Analysis used in the real life?
Emergency Response
  E.g. Analyze the areas reachable by a local fire service department within 15 minutes (driving)
  E.g. Analyze the areas reachable by residents in case a nuclear exposure in Pickering within 30 minutes (walking)
Urban Planning
  E.g. Locate the streets that are reachable by car within 15 minutes from a point in Markham -> for planning a new bypass in the city
Commercial
  E.g. Determine the area serviced by a Home Depot store within 20 mins by driving, and find areas that are not covered for planning for a potential store (Location-allocation problem)
  E.g. Flight companies want to see the areas covered by their routes within 5 hours of flight time

## Slide 6: Suppose you are a planner for the City of Markham. You want to determine the 15-minute service area serviced by all YRT buses in the city.
What travel mode are we most likely consider when creating the service areas? A) Driving; B) Cycling; C) Walking
Which of the following datasets do you need to create the service areas? Why?
(Please indicate all datasets needed)
  Bus Fare
  Bus Stop Locations
  Street network
  Vehicle Count data

## Slide 7: Example coursework (Advanced GIS - GEOG 381)

## Slide 8: Questions?

## Slide 9: 2. Tutorial
Follow tutorial here: https://www.qgistutorials.com/en/docs/3/service_area_analysis.html