## Slide 1: GIS Lesson 10
Spatial Analysis (2)
空間分析 (2)
2020/7/16

## Slide 2: Agenda
1. Today’s Class 今日課堂
2. Tutorial 個別指導
Interpolation 插補
Download a set of point data for interpolation according to your interest (e.g. weather station data, elevation data)
Examples
Demonstration in QGIS
Review – Raster Data
Make a raster output
What is Interpolation?
Review – Tobler’s First Law of Geography
Pattern Analysis – Spatial Autocorrelation
Types of Interpolation Methods
Review – Stevens Measurement Levels

## Slide 3: Review – Raster Data
Raster data is made up of _____________.
Raster data is used to display _______________ information (hint: what can you think about field data?)
The quality of the raster increases with (increasing/decreasing) number of cells and (increasing/decreasing) cell size, which means (higher/lower) resolution.
Notes: Answers:
Pixels/Grid Cells
Continuous
Increasing; decreasing ; higher

## Slide 4: Review – Raster Data
Raster data is made up of pixels/grid cells.
Raster data is used to display continuous information (hint: what can you think about field data?)
The quality of the raster increases with (increasing/decreasing) number of cells and (increasing/decreasing) cell size, which means (higher/lower) resolution.
Notes: Answers:
Pixels/Grid Cells
Continuous
Increasing; decreasing ; higher

## Slide 5: Review – Stevens Measurement Levels
Nominal: distinct categories, categories are mutually exclusive (can only be in one group but not the other), no implied relationship among categories
Ordinal: ranking of classes/categories based on some criteria (e.g. differences between classes 1 and 2 != classes 3 and 4)
Interval: measurements with fixed/equal units; no absolute zero; not absolute differences
Qualitative Data
Quantitative Data
Ratio: have absolute zero (e.g. distance)
Notes: Interval: difference between (25 and 35) C and (50 and 60) C is 10 C, but 50 C is not twice as hot as 25 C

## Slide 6: Interpolation
插補

## Slide 7: What is Interpolation?
Definition: Interpolation predicts values for cells in a raster from a limited number of sample data points. (ESRI, 2016) (由有限的數據點估計柵格的數據值)
Usage: Can be used to predict unknown values for any geographic point data, such as elevation, chemical concentrations and noise levels. (ESRI, 2016) (估計任何地理點數據的未知數據值)
You need to have a z-value field in the point data for interpolation (e.g. elevation, temperature)
Vector (Points)
Raster (Pixels)
Notes: Source:
https://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/understanding-interpolation-analysis.htm#:~:text=Interpolation%20predicts%20values%20for%20cells,chemical%20concentrations%2C%20and%20noise%20levels.

## Slide 8: Everything is related to everything else. But ______ things are more related than ________ things. (1969)
Tobler’s First Law of Geography
托伯勒的地理第一定律
Notes: Source: https://www.urisa.org/clientuploads/directory/Documents/Awards/Waldo_Tobler.jpg
Answers:
Near
Distant (far)

## Slide 9: Everything is related to everything else. But near things are more related than distant things. (1969)
Tobler’s First Law of Geography
托伯勒的地理第一定律
Notes: Source: https://www.urisa.org/clientuploads/directory/Documents/Awards/Waldo_Tobler.jpg
Answers:
Near
Distant (far)

## Slide 10: Spatial Autocorrelation (空間自相關性)
Definition: determines how well data objects correlate with other nearby objects across a spatial area.
Positive Autocorrelation (+): many similar values are located near each other (following the Tobler’s First Law of Geography)
Negative Autocorrelation (-): many different values are located near each other
Zero Spatial Autocorrelation (0): values seem to vary randomly throughout space
Notes: Source: https://docs.aurin.org.au/wp-content/uploads/sites/2/2014/09/Spatial_Autocorrelation.jpg

## Slide 11: Types of Interpolation Methods
1. IDW (Inverse Distance Weighting) (反距離權重)
  Estimates cells by averaging values (用平均值估算)
  Closer a point is to the center of the cell  More important (愈近愈重要)
  Weight = 1/distance
  No statistical model is used
  Easy to define
2. Kriging (克里格)
  Uses a statistical model with a variogram (變異圖) (determines spatial continuity of data) (You will learn more in GEOG 318)
  Calculates spatial autocorrelation by taking squared differences between points
  More complicated to define

## Slide 12: Types of Interpolation Methods
3. Trend
  Fitting a surface to the sample points when the surface gradually varies from region to region over the area of interest
  Just like fitting an equation to a statistical model, but with three-dimensions, including x-coordinate, y-coordinate and a value field (such as temperature or pollutant concentration)
4. Other Methods
  https://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/comparing-interpolation-methods.htm

## Slide 13: Examples
Predicting elevation values

## Slide 14: Demonstration in QGIS
IDW Interpolation (toolbox)
Notes: Source: https://www.qgistutorials.com/en/docs/interpolating_point_data.html#:~:text=English-,Interpolating%20Point%20Data,take%20measurements%20throughout%20the%20surface.

## Slide 15: Next class… You gotta choose…
Network Analysis
Nearest Neighbor Analysis
OR
OR any topics you want to cover
Notes: Nearest Neighbor: https://www.qgistutorials.com/en/docs/3/nearest_neighbor_analysis.html
Network Analysis: https://docs.qgis.org/3.4/en/docs/training_manual/vector_analysis/network_analysis.html

## Slide 16: Questions?

## Slide 17: 2. Tutorial
Download a set of point data for interpolation according to your interest (e.g. weather station data, elevation data)
Make a raster output